## Slide 1: The architecture of the P416 compiler
May 17, 2017 - P4 workshop, Stanford
Mihai Budiu, VMware Research
Chris Doss, Barefoot Networks

## Slide 2: P416
Newest version of the P4 language (finalized yesterday!) https://github.com/p4lang/p4-spec/tree/master/p4-16/spec
This talk is about the (reference implementation) compiler for P416
Compiles both P414 (i.e., P4 v1.0 and P4 v1.1) and P416 programs
Apache 2 license, open-source, reference implementation
http://github.com/p4lang/p4c

## Slide 3: Compiler goals
Support current and future versions of P4
Support multiple back-ends
  Generate code for ASICs, NICs, FPGAs, software switches and other targets
Provide support for other tools (debuggers, IDEs, control-plane, etc.)
Open-source front-end
Extensible architecture (easy to add new passes and optimizations)
Use modern compiler techniques (immutable IR*, visitor patterns, strong type checking, etc.)
Comprehensive testing
*IR = Intermediate Representation

## Slide 4: Compiler data flow
P416
parser
P414
parser
convert
P414
P416
v1 IR
IR
frontend
IR
ebpf
back-end
your own backend
target- specific
code
C code
BMv2
back-end
JSON
mid- end
mid- end
mid- end

## Slide 5: Compiler structure
Mid-end
Front-end
Back-end
P4
IR
IR
Target-specific
~25 distinct passes
Target-independent
~25 distinct passes
Same IR
IR with target-specific
extensions

## Slide 6: Structure
Mid-end
Front-end
Back-end
P4
IR
IR
libFrontEnd.a
main()
Fixed
Simplify IR eliminating constructs gradually
Library of pre-built passes
Mix and match
Custom

## Slide 7: Implementation details
Common infrastructure for all compiler passes
  Same IR and visitor base classes
  Common utilities (error reporting, collections, strings, etc.)
C++11, using garbage-collection (-lgc)
Clean separation between front-end, mid-end and back-end
  New mid+back-ends can be added easily
IR can be extended (front-end and back-end may have different IRs)
IR can be serialized to/from JSON
Passes can be added easily

## Slide 8: Intermediate Representation (IR)
Immutable
  Can share IR objects safely
  Even in a multi-threaded environment
  You cannot corrupt someone else’s state
Strongly-typed (hard to build incorrect programs)
DAG structure, no parent pointers
Manipulated by visitors
IR class hierarchy is extensible

## Slide 9: IR P4
Front-end and mid-end maintain invariant that IR is always serializable to a P4 program
Simplifies debugging and testing
  Easy to read the IR: just generate and read P4
  Easy to compare generated IR with reference (testing)
  Compiler can self-validate (re-compile generated code)
  Dumped P4 can contain IR representation as comments
IR always maintains source-level position
  can emit nice error message anywhere

## Slide 10: Visitor pattern
https://en.wikipedia.org/wiki/Visitor_pattern
  “In object-oriented programming and software engineering, the visitor design pattern is a way of separating an algorithm from an object structure on which it operates. A practical result of this separation is the ability to add new operations to existing object structures without modifying those structures.”
“Structure” = IR
“Algorithms” = program manipulations

## Slide 11: IR rewriting using visitors
Input DAG
Modified DAG
Dead code
New DAG
Output DAG
visitor

## Slide 12: IR definition language compiled to C++
interface IDeclaration { … }
abstract Expression { … }
abstract Statement : StatOrDecl {}
class AssignmentStatement : Statement { Expression left; Expression right; print{ out << left << " = " << right; } }
IR fields
Class hierarchy

## Slide 13: Learning the IR by example
Front-end and mid-end passes can all dump IR back as P4 source with IR as comments
/* <P4Program>(18274) <IndexedVector<Node>>(18275) */ /* <Type_Struct>(15)struct Version */
struct Version { /* <StructField>(10)major/0 <Annotations>(2) <Type_Bits>(9)bit<8> */ bit<8> major; ...

## Slide 14: v1model.p4: A P414 switch model
Parse
verify
cksum
ingress
egress
compute
cksum
deparse
A P416 switch architecture that models the fixed switch architecture from the P414 spec
Provides backward compatibility for P414 programs

## Slide 15: Testing the compiler
Dump program at various points and compare with reference
Compare expected compiler error messages (on incorrect programs)
Recompile P4 generated by compiler
Run v1model.p4 programs using BMv2 on packet traces and compare to expected output
P4
P4
P4
P4
P4
P4
P4
=
=
=
Expected output
=
stderr
errors
p4c
p4c
P4
P4
p4c
p4c
P4
json
BMv2 simulator
packet trace
packet trace
=
expected packet trace

## Slide 16: Lessons
P416 is a simple language,… but the P4 environment is complicated
  Supports arbitrary architectures
  Arbitrary functionality in the architecture
  Arbitrary extensions (extern blocks)
P416 is designed for extensibility
  Compilers must support extensibility while preserving stability
Modularity/extensibility seems to work
  At least 5 existing back-ends, for software, simulators, FPGAs, ASICs
Specification Implementation
Great community: thank you all!